## Slide 1: Measuring the Overhead of Trust Mechanisms in the X-Road Data Exchange Layer
Research plan, related work and preliminary measurements
Ruslan Neshchadimov · Supervisor: Artjom Lind · October 2026
Notes: Topic: what X-Road's trust mechanisms cost per message. Today: the question, the request path, what earlier work measured, the setup I actually use, and the first preliminary numbers with their limits.

## Slide 2: What X-Road is
Central Server
global configuration: members, trusted services
Trust services
CA · OCSP · time-stamping (TSA)
Organisation A · consumer
Security Server
signs · verifies · logs
Information system
the organisation's own service
Organisation B · provider
Security Server
signs · verifies · logs
Information system
the organisation's own service
signed messages over mutual TLS
Dashed: used in the background, not on every message.
Notes: X-Road is the data exchange layer Estonia has used since the early 2000s for public services, also used in Finland and other countries; the software is maintained by NIIS. Organisations never call each other directly: each runs a Security Server, and messages go from one Security Server to another, signed, logged and over mutual TLS. The central server distributes the global configuration: who the members are and which certificate authorities, OCSP responders and time-stamping services to trust. Those services are used in the background, not on every message.

## Slide 3: Research question
What does each trust mechanism of X-Road cost per message, in latency and in bytes, and which of that cost is paid on every request rather than deferred?
RQ1
Contribution of TLS, signing, verification, logging and time-stamping to latency and bytes
RQ2
How the contributions change with message size and with concurrency
RQ3
How much the answers depend on the environment: one host vs separate wired machines
Notes: Why it matters: post-quantum migration, decentralised PKI and threshold signatures all propose to change the trust layer, but there is no usable baseline: earlier measurements are end to end or on one machine and not broken down by mechanism, and NIIS publishes no open performance data. RQ3 is narrowed to one host vs separate machines on a local wired network; the wide-area variant is out of scope.

## Slide 4: The measured request path
Client
k6 load generator
Consumer SS (ss1)
sign request · log verify response · log
Provider SS (ss2)
verify request · log sign response · log
Echo IS
fixed-size reply
mTLS
Paid on every request
signing and verification, both directions
message log write on both servers
TLS handshake: by default once per message, connections are not reused
Deferred or amortised
time-stamping: batched over a hash chain, about 2 TSA calls per 1000 messages
OCSP: cached responses, refreshed every 20 minutes
global configuration refresh
Notes: Both Security Servers sign, verify and log on every message. Time-stamping and certificate status checking are deliberately moved off the request path (Ansper 2013, NIIS docs). In our runs the full configuration made about 2 TSA calls per 1000 messages, while the synchronous time-stamp policy makes one per message per server. The TLS handshake is per message by default: pool-enable-connection-reuse and server-support-clients-pooled-connections are both false in UG-SYSPAR, confirmed with tcpdump.

## Slide 5: What the closest X-Road studies measured
Work | Measured or established | Left open
Ansper et al. 2013 | Design of signing, OCSP caching, batched time-stamping; analytical throughput estimate | No measured per-message cost
Mironova 2017 | Central services testing; production intervals; behaviour without TSA | Cost on the message path
Taklai 2020 | Service latency through the Security Server vs direct | Which mechanism the overhead comes from
Snetkov 2023 | Post-quantum signatures in UXP: signature sizes | Effect on latency and throughput
Bakhtina 2026 (IJIS) | Threshold-signature round trip, one laptop | Breakdown; separate machines
Gap: measured end to end or on one machine, not per mechanism; NIIS publishes no open performance data.
Notes: Ansper et al. give the rationale for moving time-stamping and status checking off the request path. Mironova documents production intervals (global configuration 6 h, OCSP freshness 8 h in 2017). Taklai and Bakhtina measure end to end, on one machine in Bakhtina's case, which the authors list as a limitation. Snetkov gives sizes but no timings.

## Slide 6: Broader work used for the method
Naylor et al., CoNEXT 2014
The Cost of the “S” in HTTPS
TLS cost has two parts: connection setup and per-request work. How connections are used decides the cost per request.
Used for: separating the handshake from per-message work (configuration reuse). HTTPS, not X-Road: numbers not compared directly.
Georges et al., OOPSLA 2007
Statistically Rigorous Java Performance Evaluation
JVM timings need warm-up, independent runs, and the spread between runs reported next to the result.
Used for: burn-in and warm-up, 5 independent repetitions per grid, randomised order, IQR and range reported.
Notes: Two works outside X-Road, as suggested. Naylor et al. frame the TLS question: the handshake and the per-request work are different costs, and connection reuse decides how often the handshake is paid. Georges et al. justify the procedure: the Security Server runs on the JVM, so we warm up, repeat independent runs and report the spread.

## Slide 7: Configurations actually run
Name | What changes | What the difference to full shows
direct | Client calls the echo service, no X-Road | Whole X-Road path (not single operations)
full | Defaults: signing, logging, batched time-stamps | Reference point
nobody | Message bodies not written to the log | Cost of logging bodies only
synctsa | Time-stamp on every message, synchronously | A different policy, not “the cost of TSA”
reuse | Connections between SS kept and reused | Per-message TLS handshake
full+ss3 | Load split over two provider SS | Consumer-side limits under load
Dropped: notsa (interval outside the documented constraint) and short OCSP freshness (every request failed, gives no OCSP estimate).
Notes: Each comparison is read only for what it changes. synctsa changes when the time-stamp is taken, not just whether TSA is used, and runs on a local test TSA. reuse sets pool-enable-connection-reuse and server-support-clients-pooled-connections, as in the Finnish package; the Estonian package keeps the defaults. The short-OCSP attempt failed: the client proxy never queries the responder itself.

## Slide 8: Metrics and procedure
Metrics
p50 / p90 / p99 latency, requests per second
run-to-run spread: IQR and range
successful requests (HTTP 200)
bytes on the ss1 ↔ ss2 link only
TSA and OCSP calls per run
message-log growth per message
per-stage times from operational monitoring
Procedure
10 KB and 1 MB at 1 client; 10 KB at 4, 16, 32 clients
burn-in after each configuration change, then warm-up
1000 requests per run (200 at 1 MB)
5 repetitions per grid, random order
control run at the start of every repetition
wait for batch time-stamps, then clean the log
CPU performance mode, recorded per run
Notes: Bytes are counted with iptables counters on the consumer SS for traffic to the provider's port 5500 only. Cleanup waits until every logged message has a time stamp, so deferred time-stamping is not cut off between runs. CPU power mode turned out to matter a lot, so it is now fixed and written into each run's metadata.

## Slide 9: Testbed: three wired machines
l1 · 10.10.0.1
Central Server, test CA (OCSP, TSA), management SS, provider B (ss3) + echo
l2 · 10.10.0.2
Consumer SS (ss1) and the k6 load generator; runs the benchmark
l3 · 10.10.0.3
Provider A (ss2) and the echo information system
Gigabit switch · subnet 10.10.0.0/24 for all Security Server traffic
Each container has its own 10.10.0.x address (ipvlan): no NAT, no port publishing, no extra MAC addresses on the university network
Three Intel i5-8250U laptops; CPU in performance mode; clocks synchronised with chrony
Remote access over the university VPN; the same stand is also run on one host for comparison
Notes: The switch is also connected to the office network, which gives the laptops their university addresses for access, but traffic between the laptops is switched locally. Each container is pinned to an address in 10.10.0.0/24. For RQ3 the same stand also runs entirely on l2, so hardware and power mode are the same and only the network differs.

## Slide 10: Preliminary results, one client
Config | 10 KB p50 | Δ vs full | 1 MB p50 | Δ vs full
direct | 0.7 ms | — | 10.1 ms | —
full | 28.1 ms (IQR 1.5 %) | — | 74.1 ms (IQR 4.4 %) | —
nobody | 27.4 ms | −0.8 (noise) | 39.5 ms | −34.6 (−47 %)
reuse | 26.1 ms | −2.0 | 69.6 ms | −4.5
synctsa | 117.0 ms | +88.9 | 165.8 ms | +91.7
Same grid on one host (same CPU): 29.8 ms at 10 KB, 74.7 ms at 1 MB; per-mechanism differences agree within 1–3 ms.
Medians of 15 runs per point (3 grids × 5 repetitions). Successful requests: 15 000 of 15 000 at 10 KB, 3 000 of 3 000 at 1 MB. Control run over the night: 27.5–29.0 ms, IQR 1.4 %.
Preliminary. Three machines, 3 × i5-8250U, CPU performance mode, local test CA and TSA · night of 5–6 October 2026
Notes: Read the table as differences from full on the same night and machines. X-Road adds about 27 ms at 10 KB and about 64 ms at 1 MB over the direct call. Logging bodies matters only for large messages. The synchronous time-stamp policy is the most expensive setting, but it is a different policy on a local test TSA. Preliminary: one testbed, old CPUs, local CA and TSA, which make the numbers optimistic.

## Slide 11: Connection setup vs per-message work
≈ 2 ms
mTLS handshake per message (full − reuse, 10 KB, 1 client)
3.3 KB
fewer bytes ss1 → ss2 per message with reuse (14.8 → 11.5 KB)
≈ 26 ms
remaining per-message work: signing, verification, logging
By default X-Road opens a new TLS connection for every message. Reusing connections removes the handshake but leaves most of the cost, which is message-level.
Notes: Prompted by the advice to separate TLS setup from per-request work. reuse changes only whether connections between the Security Servers are reused, so the difference is the handshake (local network, RSA-2048 certificates). With reuse there were 3 failed requests out of about 63 000 measured, likely a pooled connection already closed by the other side; to be checked.

## Slide 12: Limitations found so far
CPU power mode
Same control run: 79.7 ms in balanced vs 28.7 ms in performance. Earlier runs are not comparable in absolute terms; the mode is now fixed and recorded.
Concurrency
At 4 to 32 clients the spread between runs is large (IQR 25–60 %), so differences between full, nobody and reuse are not resolved there.
Optimistic PKI
Local test CA and TSA on the same network; production intervals and services may differ.
Hardware and scope
Three 2017 laptop CPUs, one local network, no wide-area link. Comparisons are within one environment.
Notes: The power-mode effect was the biggest surprise: on a lightly loaded machine the CPU stayed at low clock speed, and every stage of the request was 2 to 2.5 times slower according to operational monitoring. It looked like network overhead until the stage breakdown showed that purely computational stages slowed down too. All environments are being re-measured in performance mode.

## Slide 13: Status and next steps
Done
Testbed scripted: one host or three machines
Clean grids on three machines in performance mode
TLS setup separated from per-message work
One host vs three machines (RQ3)
In progress
Same grid on the development laptop
Per-stage breakdown from operational monitoring
Next
Concurrency: throughput ceilings only
Report revision with final tables
To discuss: plain mTLS baseline? HPC VMs?
Questions and suggestions welcome.
Notes: Final results are expected by the end of the week. The one-host run on l2 uses the same CPU and power mode as the three-machine run, so the difference between them isolates the network. Concurrency results will be reported as ceilings with their spread.